PBX-System

Short User Guide

AC 14 analog

Introduction

Get Started

Connect the plug at the end of the  power supply into the socket labelled with the power symbol (       ) until you hear it click.

Connect one end of the analogue connection cable into the socket labelled "AMT" until you hear it click in place.

Connect the other end of the cable to the socket of the network provider or the installed socket.

Connect the plugs of your telephone equipment to the telephone system.

The default setting of the AC 14 analog  is that the first connection is extension 11 and the se- cond connection is extension 12.

Plug the power supply into the 230V main socket. The red LED will flash while initialising and then light up.

To enter your phone number, see below.

You now can make calls. After lifting the telephone receiver you will hear the dial tone of the telephone exchange.

An incoming call  will ring extension 11, 12, 13 and 14.

2

Introduction

Table Of Contents

Short User Guide ........................................................................................................................ 1

Get Started ................................................................................................................................. 2

Enter your Phone Number quickly ............................................................................................. 2

Table of  Contents ....................................................................................................................... 3

Important notes on using analogue equipment .......................................................................... 4

Pictograms and Buttons ............................................................................................................ 5

LED´s of the AC 14 analog ......................................................................................................... 5

Fax Switch ................................................................................................................................. 6

Check Delivery Contents ............................................................................................................ 7

Connections of AC 14 analog ...................................................................................................... 7

Safety Notice .............................................................................................................................. 8

Mains Socket .............................................................................................................................. 8

Connecting extensions to separate  sockets .............................................................................. 9

Connect Analogue Extensions .................................................................................................... 9

Wallmounting ............................................................................................................................. 9

Activate the FAX switch ............................................................................................................. 10

Making a call - spontaneous seizure with internal (factory setting) ........................................... 11

Internal call waiting ................................................................................................................... 11

External call waiting .................................................................................................................. 11

Call waiting cancel .................................................................................................................... 12

Internal Transfer without announcement ................................................................................. 12

Brokers Call .............................................................................................................................. 12

Callback when free .................................................................................................................... 12

Pick Up an external call ............................................................................................................. 12

Internal Transfer with announcement ...................................................................................... 12

Time Accounts .......................................................................................................................... 14

Set Call Barring ......................................................................................................................... 16

Program Exceptions Codes ....................................................................................................... 17

Establish an  USB Connection ................................................................................................... 18

Configure your AC 14 analog ..................................................................................................... 18

Declaration  of  conformity ........................................................................................................ 19

3

Introduction

Important Notes On Using Analogue

Equipment

Only analogue apparatus which are approved to be connected to the Public Switched Telepho- ne Network (PSTN) may be connected to the analogue side of the system.

This includes all 2 wire telephones, answering -, fax machines, and modems.

The system supports both dialling method Loop Disconnect (LD) or Dual Tone Multi Frequency

(DTMF). DTMF is a faster dialling method. The system will dedect the dialling method automatically.

From an analogue phone, you can call any extension free of charge by dialling the

internal phone number. You can call an external number after seizing an outside line. To do this dial 9 to get an outside line and then dial the telephone number required.

If you set “spontaneous exchange line seizure with internal ” for your telephone extension then you must press the hash button before the internal phone number. Note in this mode you cannot call an extension if your phone is an older LD or rotary type dial phone.

To carry out system functions, your phone must have a STAR Button (*). The sequence to

enter will be * followed by the function number. If your phone is an older type LD phone then you can dial 99 instead of  * .

To make an enquiry call your phone must have an R Button (Recall Button). The signalling for this must be set to Timed Break Recall (TBR). On older rotary dial phones you do not need to press the R Button when making an enquiry call. System functions such as last number redial, abbreviated dialling etc, can be carried out from any LD phone.

You can also use the functions of a standard analogue telephone (e.g. redial, abbreviated

dialling) in conjunction with your telephone system. Please refer to the operating instructions for the telephone concerned for details of these functions.

Details of how to operate the functions of your telephone system that you are able to use from a standard analog telephone set to DTMF are given in the  instruction manual.

Each programming entry will be acknowledged by a confirmation tone. If this tone is not received or if an error tone is returned then you must repeat this entry.

Please ensure that your provider has disabled meter pulses to avoid any interference on your phone calls.

For data transfer via the analogue ports, the telephone system supports the V.90 standard (up

to 56600 bps, a reduction in speed is possible due to transmission path and cables used, down

to 28800 bps V.34). When operating a modem, it is imperative to configure the modem to blind

dialling because most modems do not detect the dial tone of a telephone system. On modems that operate with the Hayes command set, blind dialling is set by means of the X0..X4 parameters

4

Introduction

Pictograms And Buttons

All operations and functions of the telephone system are explained in clear and  easy to follow pictograms.

Pictograms

A	Ringer

h	Pick up receiver

Z	Dial Phone or Code

Number

Q	Acknowledgement tone

T

Conduct a call

ª

Replace receiver

K

Conference

®

Room monitor

Buttons

r

9

Recall Button

Number Button for entering digits, e.g. „9“

S	Star Button for functions

R	Hash Button to dial extension when automatic line seizure is active

LED´s Of The AC 14 Analog

LED 1	LED 2	LED 3

Permanently lit

Flashes

LED 1 (red)

LED 2 (green) LED 3 (green)

System  is  operational

System  connected  to  the phone  network

System  is  connected  to  the

computer  via  USB

System  being  initialised

Inward or outbound call

Data  being  transferred

5

Introduction

Fax Switch

A fax switch is a device or feature of a device that recognises the difference between telephone and fax calls. The fax switch automatically forwards telephone and fax calls to the correct extension.

Your “AC 14 analog” is fitted with a fax switch which you can set conveniently in TK Suite or via a programming procedure (see page 10).

You have the option of choosing between 3 operating modes: Active, Passive or Inactive.

ACTIVE:

If you set the fax switch to “Active”, the PBX takes an external call, checks whether it is a fax and then forwards it to the default extension if required.

PASSIVE:

If you set the fax switch to “Passive”, the fax switch checks all calls in the background which have already been taken by a telephone or an answering machine. If the call is a fax,

it is then forwarded to the default extension automatically. The extension which took the call originally will automatically receive a busy tone.

INACTIVE:

The fax switch is disabled.

Note

In ‘Active‘ mode, the fax switch will answer all incoming calls automatically on the second ring and then will ring the relevant extension phone. Please note that in this mode the incoming caller will be charged for the call. This is regardless whether the caller was able to speak to the relevant extension. During this connection process the caller will hear a system generated ringing tone, this may differ from the normal exchange tone generated.

6

Installation

Check Delivery Contents

-  1 PBX System

-  1 230 V-Power Pack

-  1 connection cable to analogue exchange, length 1,5 m

-  1 PC-USB connection cable, length 3 m

-  2 plugs and screws

-  1 manual

-  1 CD-ROM with TK-Suite

Connections Of AC 14 Analog

Connection for

Power Pack

USB Connection

Port 1

Extension No. 11

Port 2

Extension No. 12

1  2  3 4  5  6  7  8

connection to

analogue network

1      2       3      4     5      6      7      8

Port 1, Extension No. 11

Port 2, Extension No. 12

Port 3, Extension No. 13

Port 4, Extension No. 14

7

Installation

Select  Location

Install the System in a dry room free of any hazardous materials. Avoid sites near air

conditioners, radiators, equipment with excessive high radiation, direct sunlight, excessive dust and the danger of liquid spillages such as water or chemicals.

Ambient temperature 5C to 30 C. Max humidity 70% non condensing.

The distance of the equipment to other objects such be considered to guarantee an air circulation. The minimum clearance distance of 50 cm should be adhered to. The distance

of the system to the mains socket and the telephone network socket should not be more than 1 meter. (Length of mains cable 1.20 m)

It must be made possible to place a Laptop or PC near the telephone system for programming.

Mains  Socket

On power failure the PBX System is without function. Use the provided Power Pack only. Model No.: TST 1100468

Safety  Notice

The telephone system is for the connection to an anlogue line.

You may connect any analogue apparatus to the system which you are allowed to connect to the Public Switched Telephone Network (PSTN).

Any other use of the system which does not comply with the aforesaid is prohibited. The system has a General European Connection Licence.

-  The system conforms to the specified conformity and safety regulations.

-  Warning! The telephone system must have a functional electrical earth.

-  DANGER! Please disconnect the apparatus from the mains socket before connecting extensions and lines to it.

-  Do not connect or disconnect any lines during a thunderstorm.

-  Install all cables so that no one walks or trips over them.

-  Ensure that no liquids can enter the system as otherwise short circuits maybe the result.

-  No liability will be accepted for consequential loss or damages such as call charges for unintentional calls or connections.

-  No calls can be made during a power failure. We would suggest to install surge protectors

to all lines or extensions which do not originate within the main building.

8

Installation

Connect Analogue Extensions

You may connect up to four analogue apparatus to the system which have been approved for

connection to the public switched telephone network. a/b-Apparatus is:

- Telephone (2 wire Phone or POT) either LD or MF Dialling with Timed Break Recall (TBR)

(60 – 800 ms)

- LD Phones may only have limited feature access.

- Fax machines Group 3

- Telephone Answering Machines

- Modem 56k (V.90 to 56600 bps, may reduce to 28800 bps due to quality of lines V.34)

Connect the analogue apparatus via 2 wires to the a and b wire (Speech Pair) of the system port

Wall  Mounting

- Mark two vertical drill holes 92 mm apart on the wall.

- When marking the drill holes, make sure that there are no concealed lines at these points

(gas, water pipes, electric cables or similar).

- Drill the two holes.

- Insert the wall plugs so that they are flush with the wall.

- Screw in the two screws leaving the head protruding by about 4 mm.

- Hang the telecommunications system on the screws and pull it down on the wall until it snaps into place.

Connecting  Extensions  To  Separate

Sockets

If you want to connect your extensions to separate sockets, you will find the connection panel for the plug-in extensions on the underside of your AC 14 analog. Unplug the power pack from

the 230 V mains socket before working on the connection panel. The assignment of the

extension connections is displayed on the connection panel. To ensure perfect functioning of

the telecommunications system and the connected extensions, you should connect the terminals either to the sockets or the plug-in terminals! This means that if a extension is connected directly via a socket, e.g. connection 1, no second device should be connected via

the terminals  at the same extension connection, e.g. La1/Lb1. The connections La and Lb of the plug-in extensions are connected with connections 1 and 2 of the separate sockets. You can use commercially available telephone lines for the connection. We recommend: Telepho-

ne lines length between telecommunications system and sockets: max. 800 metres at 0.6

mm wire diameter.

9

Installation

Activate The FAX Switch

Start programming mode with: h*PRO(System-PIN)	qª

PRO

h	*3292

4   Inactive

2   Active	q	ª

7   Passive

Lift receiver

FAX switch activation

Acknowledgement tone

Replace receiver

Continue programming or end programming:h*ENDqª

END

Enter Extension Number Of FAX

Start programming mode with: h*PRO(System-PIN)	qª

PRO

h	*3294	z	q	ª

Lift

receiver

Extension number

of FAX

Enter  two  digit

extension  number

Acknowlegement

tone

Replace

receiver

Continue programming or end programming:h*ENDqª

END

Factory  Settings

-  Incoming calls will ring extensions 11,12, 13 and 14

-  Extension numbers: 11, 12, 13, 14

-  External Line  Access: Full access for all extensions

-  External Line seizure: Spontaneous seizure with internal

-  Day Service: No entry

-  Night Service: No entry

-  Call Waiting: Not enabled on extenions 11,12 and 14. Call Waiting is enabled for extension

13.

-  Internal Call Forwarding: Off

-  CLIP: On

-  MoH: Internal

-  Automatic Dial: Off

-  Time Accounts: No Time Accounts set

-  Disconnect on Limit reached: Off

-  System-PIN: Not activated

-  Clock: Not set

-  FAX Switch: Inactive

-  Terminal Types: Extensions 11 and 12 are set to telephone, extension 13 answering machine and extension 14 to multifunctional device.

10

Quick Reference

Making A Call - Spontaneous Seizure

With Internal (Factory Setting)

h	q  z	q	t

External

call

Lift receiver

External dial tone

Enter external phone number

Ringing tone	External Party answers, conduct call

The spontaneous external seizure (seize outside line) is only possible directly after lifting the receiver. If you want to make an external Enquiry during an internal call, you have to seize the

external line by dialling 9.

h	q         #         q	z         q	t

Internal

call

Lift receiver

External dial tone

press hash- key

Internal dial tone

enter Exten- sion number

Ringing tone	Extension answers, conduct call

Making A Call - External Seizure With

"9"

External call

h  q	9	q	z	q	t

Lift receiver,

internal dial tone

Seizure with "9"

External

dial tone

Enter

external phone number

ringing tone	External party

answers, conduct call

Internal call

h  q	z	q	t

Lift receiver,

internal dial tone

Enter extension

number

ringing tone	extension answers,

conduct call

Internal  Call  Waiting

t         q	ª	a	h	t

You are on a call and hear the call waiting tone

end the call

automatic ringing by the waiting party

Lift the receiver	conduct the call

External  Call  Waiting

t         q	r	9	t

You are on an internal

call and hear the call waiting tone

Press R, the call is

placed on hold

Fetch the waiting

external call

conduct the call

Reject A Waiting Call

t  q	r	*229	t

You are on a call and hear

the call waiting tone

Press R, the call is placed

on hold

Reject the waiting

call

Continue your call

11

Quick Reference

Call Waiting Cancel

2  disable

h	*  265	q	ª

Lift receiver

Call waiting cancel

3  enable

Acknowledgement tone

replace receiver

Internal Transfer With Announcement

t                r	z                t	ª

Conduct

external call

enquiry, external call is

placed on hold

Enter internal

phone number

Announce external call	transfer external

call

Internal  Transfer  Without

Announcement

t                r	z                ª

Conduct external  enquiry, external is

Enter internal

transfer external

call

placed on hold

phone number

call

Pick Up An External Call

a	h	*463	t

External call on - another telephone

Lift the receiver

Pick up external call

Conduct call

Brokers  Call

t	r	z                t                r	p

Conduct first Call

Enquiry first call is placed on hold

Enter extension number

conduct call	Enquiry, both calls are placed on hold

with  "9" to external call

or with extension number to internal call

Callback When Free

h	z	q	r	*783	ª

Lift receiver	Enter extension number

Busy tone	Enquiry	Callback when free	Replace receiver.

12

Quick Reference

Enter Wake Up Time

h  *  9327	7z	6z	q	ª

Lift receiver Enter Wake Up Time

Enter hour in two

digits

Enter minutes in two

digits

Acknowledgement

tone

Replace

receiver

After Entering the Wake Up Time, Wake Up call is activated for all days.

Set Wake Up Days

You can specify on which days the Wake Up Call will be triggered on your telephone after you have entered an alarm time.

h	S9327	9ZEnter digits according to the following list	#ª

0 = all off

8 = Monday to Friday

9 = Monday to Sunday

1..7 = Monday .. Sunday

You can enter several days in sequence. If, for instance, you want to activate the Wake Up call for Monday, Wednesday and Friday, use the following approach:

h	S93279	1	3	5	#	ª

Monday	Wednesday	Friday

After entering the Wake Up Days, Wake Up Call is activated for this days.

Switch On Wake Up Call

h  *  9322	q	ª

Switch on Wake Up Call is needed, to

reactivate a deactivated Wake Up call.

Lift receiver   Code to switch on Wake

Up Call

Acknowledgement

tone

Replace

receiver

Receiving A Wake Up Call - Stop Wake

Up Call

h                ª

Lift receiver

Replace receiver

Switch Off Wake Up Call

h  *  9323	q	ª

Lift receiver   Code to switch off Wake

Up Call

Acknowledgement

tone

Replace

receiver

13

Quick Reference

Receiving A Wake Up Call - Activate

Snooze Function

After completion of the procedure ‚Continue Wake Up Call‘ the phone will ring every 10

minutes for a one hour period.

h  *  9329	q	ª

Lift receiver   Code to activate snooze

function

Acknowledgement

tone

Replace

receiver

Set  Time

Start programming mode with: h*PRO(System-PIN)	qª

h  *846	7zEnter hours (two digits)

6z	Enter Minutes (2	qª

digits)

Continue Programming or end Programming:h*ENDqª

Set  Date

Start programming mode with: h*PRO (System-PIN)	qª

h  *328  8z

Enter Day (2

digits)

6z Enter Month (2

digits)

5z Enter  year (two     qª

digits)

Continue Programming or end Programming:h*ENDqª

Show Time

You can have the time of day displayed on a CLIP telephone. After completing the procedure,

the time is shown for up to 60 seconds – depending on the type of device used - on the display

of the telephone that has been hung up. Wile showing the time, the displaying telephone rings.

h  *847	q	ª

The time is shown up to 60 seconds on the display

Show time	Acknowledgement tone	replace receiver

Time Accounts

You can set up a time account for external connections for each internal party. Furthermore, you can specify what should happen when the time limit is reached for each party: should the internal party be allowed to finish outside calls without being cut off, but not be allowed to

make any more external calls, or should the call be cut off immediately. The party will first be allowed to make external calls again when the time limit has been cleared. Exception: the direct number can still be called after the time limit has been reached.

Time accounts are protected by a special PIN (Personal Identification Number).

Delivery status: PIN - No entry, Time Limit - No entry, Disconnect on limit reached - Off.

14

Quick Reference

Time Account Menu Start/Stop

You can protect access to the time account menu by entering a 4-digit account PIN. If your

hear the engaged tone on entering the menu, enter the account PIN. If you hear a short confirm tone, no PIN has been set for this time account.

If you have forgotten the Account PIN, you can change it on your PC in TK Suite Set (Security Properties/Code Digits). If the time account is initiated, you hear a special dialling tone when you pick up the receiver.

Start Time Account Menu

h	*657

(zEnter Account Pin	)	q	ª

Lift receiver

Start Time

Account Menu

Acknowledgement tone

Replace receiver

Stop Time Account Menu

h	*END	q	ª

Lift

receiver

Stop Time Accout

Menu

Q - Ton

Replace

receiver

Enter / Delete Account PIN

Start Time Account Menu with *567

3 Enter	7zEnter new Account

h	*746

5 Delete	q	ª

Lift receiver

Enter/ Delete

Account PIN

Acknowledgement tone

Replace receiver

Stop Time Account Menu with *END

Enter / Delete Time Limit

Start Time Account Menu with *567

3 Enter

2z#

h	*546

5 Delete

4z	q  ª

Lift

Enter or delete

Extension

Enter Time Limit in

Acknowledgement Replace

receiver

Time Limit

number you want to set or delete a time limit for.

minutes that the extension shall be able to make external calls and conclude input with

#.

tone

receiver

Stop Time Account Menu with *END

15

Quick Reference

Switch Disconnect On Limit Reached

On / Off

Start Time Account Menu with *567

3 On

h	*873

2 Off	q	ª

Lift receiver

Disconnect on Limit

Reached

Acknowledgement tone

Replace receiver

Stop Time Account Menu with *END

Locking / Unlocking  Your Phone

h	*724 (Telephone-PIN)	2

Unlock phone	q	ª

Lift receiver

Telephone lock

3  Lock phone

Acknowledgement tone

Replace receiver

Pogramming Telephone PIN

h	*746 (Telephone-PIN)	3 Enter	7  z	q	ª

5 Clear

Lift receiver

Program PIN

Enter old PIN

Enter the new 4-digit

PIN (0000 to 9999),

Acknowledgement tone

Replace receiver

Set Call Barring

Start Programming mode with: h*PRO

(System-PIN)  qª

h	*237

Lift receiver	Call Barring

8

4

6

2

5

Select

Full

National Internal  only Local

None

4z	q	ª

Enter extension Number   Confirmation   Replace

Service

for which the access should be valid

tone

receiver

Continue programming or end programming mode:h*ENDqª

16

Quick Reference

Program  Exceptions  Codes

Start Programming mode with: h*PRO

(System-PIN)   qª

3  Enter

8z	#

h  *373	4z	q	ª

Lift receiver

Exceptions Codes

5  Delete

Enter Index 0 to 9

Enter STD code, max 6 digits

Confirmation tone

Replace receiver

Continue programming or end programming mode:h*ENDqª

Enter Barred Numbers

Start programming mode with: h*PRO  (System-PIN)	qª

h	*773

3  Enter

5  Delete

8z	#

4z	q	ª

Lift receiver

Barred numbers

Enter Index 01 to

20

Enter STD Code, max 6 digits

Confirmation tone

Replace receiver

Continue programming or end programming mode:h*ENDqª

Assign Barred Number (To Extensions)

Start programming mode with: h*PRO

(System-PIN)    qª

h  *989

2  Off

3  On

4z	q	ª

Lift receiver

Assign Number

Enter Extension

Number

Confirmation tone

Replace receiver

Continue programming or end programming mode:h*ENDqª

17

Communication via PC

Establish An USB Connection

You may connect the telephone system with a PC or Notebook via the USB connection.

(Not supported with Windows NT 4.0)

1.  Take the supplied USB Cable. You will identify this on the USB Symbol on the plug.

2.  Plug in the square plug of the USB cable into the USB socket of the telephone system

3.  Plug in the flat plug of the USB cable in one of the USB connections of your computer

4.  Switch on your computer

5.  On start-up of Windows with the telephone system, you will be requested to enter the location of the driver.

IMPORTANT! It may be that during the installation you will be asked to insert the CD of the operating system. Therefore it will be advisable to have this CD to hand.

6.  Once the PC has identified the connected telephone system, the hardware assistant will

be displayed. The hardware assistant will install the software for the new Hardware components (AC 14 analog). Click on ”next”

7.  In the following dialog window select find  “suitable driver” for hardware (recommended).

8.  Enable the option “CD-ROM Drive” and de-select all other check boxes. Insert the CD

“Communications Software” with the USB Drivers in the CD-ROM drive and click on

“next”.

9.  After the driver has been found click on next to start the installation.

10. Drivers being installed

11. Insert the Operating System CD if asked to do so, to install the USB support.  After the

software has been installed click on “finish”.

12. Restart your computer to complete the installation.

Configure Your AC 14 analog

You can configure your AC 14 analog with a few mouseclicks, after connecting it to a PC:

-  Start "TK-Suite Mini" on your AGFEO CD.

-  Set Interface to "USB direct connection"

-  Click on "Get and edit PBX configuration"

-  Edit the configuration

-  Click on "Send Configuration" to send the configuration to the AC 14 analog

-  If you want to revert to the latest configuration, click on "Revert to latest sent configuration".

Use TK-Suite Basic to make full use of all the features of your AC 14 analog, such as CTI, Call Filters or editing the Phone Book.

# Text boxes

Bedienung	1

Installation

Installation

t  p

z

Installation

Installation

Installation

PIN

Installation

Installation